Section 110 of the Standard Specifications for Highway Construction, Edition of 2003, is hereby deleted and the following substituted therefore:

110.01 General. This work shall consist of measures taken to prohibit the degradation of water quality and wetlands. The purpose is to limit, control, and contain fill materials, soil erosion, sedimentation, and other harmful wastes resulting from construction operations that could result in harm to the wetlands and waters of the United States. These requirements apply even if Corps of Engineer (C of E) Section 404 or National Pollutant Discharge Elimination System (NPDES) Permits are not required for the project.

These requirements apply to all activities under the Contract. The Contractor should be aware that requested modifications to the Contract and/or individual permits may not be approved.

The Contractor must comply with all applicable Federal, State, and local permits and requirements on sites outside of the right-of-way limits utilized by the Contractor for the benefit of the project. While the primary enforcement of these requirements for locations off of the right-of-way rests with the applicable regulatory government agency, the Department retains the right and authority to inspect and enforce Contractor compliance should violations come to the attention of the Department.

110.02 Responsibility of the Contractor. The Contractor shall comply with the requirements of the Federal Water Pollution Control Act, 33 USC § 1251 et seq., the Arkansas Water and Air Pollution Control Act, Ark. Code Ann. § 8-4-101 et seq., and the regulations, orders, or decrees issued pursuant thereto. In the event of conflict between these regulations, orders, or decrees and the provisions shown on plans, the more restrictive requirements shall apply.

110.03 C of E Section 404 Permit for Department Right-of-Way and Contractor Facilities. (a) General. All requirements of the Contract and Specifications shall apply to the Contractor's activities covered by the Department's C of E Section 404 Permit on or off the right-of-way. Section 404 of the Federal Water Pollution Control Act, as amended, establishes a permit program for the regulation of discharges for dredged or fill material and excavation in wetlands and other waters of the United States.

b) Responsibility for Initial Permit. The Department will obtain all required Section 404 Permits for essential work on the right-of-way before the Contract is awarded. Contract documents will detail the location and amount of permanent and/or temporary fills, excavation, and clearing activities allowed under the permit.

(c) Contractor Requested Permit Modifications. The Contractor shall submit a request on a form provided by the Department to the Engineer for any activity involving wetlands or waters of the United States on or off the right-of-way and not covered by the Department's C of E Section 404 Permit prior to performing the activity. The Contractor shall be prepared to prove there is no practicable alternative to the Section 404 Permit change being requested. The Engineer will make a determination within 10 business days concerning the necessity or practicability of the request. The Department will then apply for permit modifications it determines to be necessary or practicable. The C of E review of proposed modifications to a Section 404 Permit may require 60-120 calendar days. These requested changes may be denied or modified by the Department or C of E.  Requested modifications that require mitigation will be denied by the Department. If the Department declines to consider a Permit modification request by the Contractor for an off right-of-way activity, the Contractor may apply for his own Section 404 Permit.

(d) Compensation and Extension of Contract Time. The Contractor will not be granted additional compensation or contract time due to requested modifications to the Section 404 Permit that are considered by the Engineer to be for the convenience of the Contractor. If, due to no fault of the Contractor, a Section 404 Permit modification involving on right-of-way activities is deemed by the Engineer to be necessary, additional contract time and/or compensation may be considered according to the provisions of Section 104.

110.04 NPDES Permit. (a)General. Federal requirements mandate that excessive amounts of pollutants be prevented from exiting construction sites. The Arkansas Department of Environmental Quality (ADEQ) has issued the NPDES Permit for owners of facilities discharging storm water associated with construction activity located in the State of Arkansas (Permit).  Copies of the entire Permit are available from ADEQ.

A NPDES discharge permit is required for all construction sites that will result in the disturbance of one acre or more, by activities such as clearing, grading, or excavating, in accordance with the following:

- Automatic Coverage (Small Construction) Sites: Automatic Coverage applies to any construction activity that will disturb/expose a total of one acre or more, but less than five acres.  This also applies to any construction activity that will disturb/expose less than one acre, if it is part of a larger site that will ultimately disturb/expose one acre or more.

- Large Construction Sites:  A project meeting the definition of a “large construction site” is any construction activity that will disturb/expose a total of five acres or more.

The Department will obtain Permit coverage for essential work on the right-of-way before the Contract is awarded.

(b) Storm Water Pollution Prevention Plan. The Department will develop a Storm Water Pollution Prevention Plan (SWPPP) for the project as required.  Any measures required by the SWPPP are included in the plans, specifications, supplemental specifications, and special provisions.  The Engineer will maintain the SWPPP at the project field office or, if a field office is not provided, the SWPPP will be maintained at the office of the Resident Engineer.

The Contractor shall be responsible for compliance with all applicable terms and conditions of the Permit as it relates to activities on the construction site, including protection of endangered species and implementation of Best Management Practices (BMPs) and other controls required by the SWPPP.  A special provision for the protection of endangered species will be a part of the Contract, if applicable.

The Contractor shall inform the Engineer sufficiently in advance of planned construction activities and conduct construction activities in a manner to allow the SWPPP to be modified to accommodate the activities.

The Engineer will provide the Notice of Coverage (NOC) to the Contractor to post on the project at a safe, publicly accessible location near where construction is actively underway, and move it as necessary to comply with the Permit public notice requirements.

Prior to beginning work on the project, the Contractors shall complete the Contractor Identification section of the Storm Water Pollution Prevention Plan as required by Part II.A.5 of the Permit.

All off-site areas, including storage sites or borrow areas or waste areas, are operated by the Contractor.  The Contractor shall be responsible for obtaining any required NPDES permits for off-site areas.  Off-site areas within city limits are subject to city planning regulations and may require clearance from the city. Off-site areas that fall within the jurisdiction of a “qualifying local program” as defined in the Permit, must comply with the requirements of the local program.  The Contractor shall obtain clearances and approvals of this type for their off-site areas.

The Permit obtained by the Department for the project does not cover discharges from dedicated asphalt and dedicated concrete plants operated by the Contractor for, or located on, the project.

(c) Controls and Measures.  All controls are designed and installed with the primary goal of retaining sediment on site to the maximum extent practicable.

The sequence of major activities, the erosion and sediment control items associated with the major activities, and the timing of implementation for those items are required for the SWPPP. The Contractor shall submit information related to the planned sequence of major activities in writing to the Engineer at the preconstruction conference for incorporation into the SWPPP by the Engineer. Amendments to the planned sequence of major activities shall be submitted in writing to the Engineer sufficiently in advance to allow incorporation into the SWPPP.

The Contractor shall provide information on locations of the following in writing to the Engineer at the preconstruction conference and/or sufficiently in advance of installation to allow incorporation into the SWPPP:

- Stabilized or wheel washing vehicle exits from the construction site as required to prevent tracking of material onto the public roadway.

- Temporary sanitary facilities provided and properly maintained by the Contractor.

- Concrete washout waste areas to be utilized to prevent concrete waste from being discharged into water bodies.

- Storage areas for fuel and other potentially hazardous materials and truck washing areas with appropriate controls to prevent non-storm water discharges.

(d) Non-storm water discharges.  The Contractor shall not release any materials except the following non-storm water discharges that are authorized by the Permit:  discharges from fire fighting activities; fire hydrant flushings; wash water (without detergent or spilled material); water used to control dust; potable water sources including waterline flushings; irrigation drainage; air conditioning condensate; springs; uncontaminated ground water; and foundation or footing drains where flows are not contaminated.

All other non-storm water discharges are prohibited unless in compliance with and covered by a separate NPDES permit.

(e) Releases in excess of reportable quantities.   Instructions to be followed after the release of a hazardous substance or oil are provided in Subsection 107.01(f) of the Standard Specifications and subsection 110.06(c) of this supplemental specification.

The Contractor shall submit all required information as soon as possible, but no later than 72 hours after knowledge of the release, to the Engineer for further submission to the appropriate agencies.

The Contractor shall submit to the Engineer, within five calendar days of knowledge of the release, a written description of the release (including the type and estimate of the amount of material released), the date that such release occurred, the circumstances leading to the release, and steps to be taken in accordance with the Permit for forwarding to ADEQ.

110.05 Standard Conditions. (a) General. The following conditions are required on all projects for the protection of water quality and wetlands:

- Compliance with all conditions of the C of E Section 404 permit, NPDES permit and Section 401 Water Quality Certification.

- To the maximum extent practicable, discharges of dredged or fill material into waters of the United States shall be avoided or minimized through the use of other practicable alternatives.

- Construction activities shall not cause unacceptable interference with navigation.

- No activity shall substantially interrupt the movement of the species of aquatic life native to the waterbody, including those species which normally migrate through the area.

- Under a Nationwide Section 404 Permit, no activity shall occur in a component of the National Wild and Scenic River System, or in a river officially designated by Congress as a "study river" for possible inclusion in the system, while the river is in official study status. Individual permits shall be obtained for activities occurring in these rivers.

- No storage of petroleum, other chemical products, waste materials, trash, etc., shall be allowed within 100 feet (30 meters) of a wetland or waterbody boundary or elevation as shown on the plans. The Engineer reserves the right to limit the storage of any material within the floodplain of a stream to preclude the possibility of an unlawful discharge to the stream.

- To move clean water around the construction area without causing additional turbidity or sediment, the use of construction staging, cofferdams, pipe culverts, lined channels, sandbagged material, barrier wall, or other suitable materials as approved by the Engineer, shall be utilized for directing or confining water from the work area. This water shall be returned to the waterbody downstream from the construction site. The options utilized should consider the minimization of sedimentation and turbidity as a primary objective.

- If material or debris resulting from Contractor operations enters a waterway, it is considered an unpermitted fill material under the C of E Section 404 Permit and the Engineer shall determine whether it may remain. If it is determined that the material is to be removed from the waterway, the Engineer shall approve the Contractor's method of removal. Options for removal should consider the minimization of turbidity as a primary objective.

- No asphaltic material shall be disposed of in wetlands or waters of the United States.

- Temporary bridges or other structures shall be used whenever it is necessary to ford any body of water on the project more than twice in any six-month period.

- Equipment shall not be operated in any body of water on the project except when required to construct channel changes or structures.

- Cofferdams needed for work in water shall be constructed from non-erodible materials.

- Materials excavated during bridge construction shall be placed on dry land outside the channel banks of all streams, at least 10 feet (3 meters) from the channel banks of a perennial stream, and at least 25 feet (8 meters) from the channel banks of a 5 Cubic Feet/Second (CFS) or larger stream. This includes channelized streams and relief channels. This material shall be properly contained or stabilized to minimize erosion and degradation of water quality and be removed before the beginning of the wet season.

(b) Wetland Areas. Wetland areas on and off the right-of-way shall be preserved and protected whenever possible. Work in or near wetlands shall be performed in a manner that will minimize harm to the wetlands. The Contractor shall be responsible for the protection of adjacent wetlands.

- Clearing of wetlands shall be limited to the minimum necessary for the completion of the project.

- Wetland areas inside or outside the construction limits shall not be used for storage, parking, access, borrow material, haul roads or any other construction support activity unless specifically approved in advance by the Engineer and according to the applicable Section 404 Permit.

- When heavy equipment is working in wetlands, appropriate measures such as placing the equipment on mats, shall be taken to minimize soil disturbance.

- Material shall not be wasted or temporarily stockpiled in wetlands.

(c) Temporary fill.

- Unless otherwise provided, temporary work ramps or haul roads, when permitted, shall provide sufficient waterway openings to allow the passage of expected high flows during the time the ramp or haul road is in place.

- Temporary fills or structures, if washed downstream, are considered to be unauthorized fill under the C of E Section 404 Permit and the Engineer shall determine whether it may remain. If it is determined that the material is to be removed from the waterway, the Contractor shall submit the proposed method of removal to the Engineer in writing for approval. When considering options for removal, the Contractor shall consider the minimization of turbidity as a primary objective. Replacement of washed fill may require a Section 404 permit change or an additional permit.

- All fill for temporary work ramps or haul roads placed within the channel banks of a stream, within 10 feet (3 meters) of the channel banks of a perennial stream, and within 25 feet (8 meters) of the channel banks of a 5 Cubic Feet/Second (CFS) or larger stream, shall be constructed using a riprap of the size specified in Subsection 816.02(a)(2), or larger material. This includes channelized streams and relief channels. A minimal amount of clean stone or gravel may be placed on top of the temporary fill in order to obtain a smooth working surface. The clean stone or gravel utilized shall have less than twelve percent passing the #200 (0.075 mm) sieve. Upon removal, salvaged material that meets the requirements of Subsection 816.02 will be paid for when reused in areas which require the utilization of riprap.

- Unless specifically authorized under the Section 404 Permit as temporary or permanent fill material, bridge demolition rubble shall not be dropped into a waterbody or wetland.

- All fill material shall be free from toxic pollutants in harmful amounts.

- All temporary fills shall be removed and the affected areas returned to their preexisting elevation.

- All temporary fill in any body of water or wetland shall be properly contained or stabilized to minimize erosion and degradation of water quality.

(d) Erosion and Sediment Control. The Contractor shall install, construct, and maintain erosion and sedimentation control items as shown on the plans or as directed by the Engineer.

- The Contractor shall install, construct, repair, and maintain erosion and sedimentation control items within three business days of being instructed to do so by the Engineer.  However, if heavy equipment is required and the Engineer agrees that conditions do not permit heavy equipment to be used, a longer time frame may be allowed.  The Contractor shall submit adequate documentation to the Engineer that proves that conditions are not suitable for the use of heavy equipment and that for there is no alternative to its use.  When conditions become suitable, as determined by the Engineer, the Contractor shall proceed with the required actions to be completed within three business days after receiving notification.

- Minimizing time of exposure of disturbed ground is a primary objective. Therefore, disturbing an area and postponing subsequent work could result in the Contractor being required to stabilize the area at no cost to the Department. Unless modified on the plans or directed by the Engineer, the total surface area of disturbed soil on the right-of-way at any one time shall be limited to a maximum of 25 acres (10 hectares). Disturbed soil is defined as exposed bare soil denuded of vegetative cover or lacking stabilization. Stabilized soil is defined as soil that is covered by grass, seeded and mulched, mulched, covered by erosion control matting, or covered by permanent stabilization as shown on the plans or as directed by the Engineer. The Engineer will have the authority to increase or decrease the limitation on surface area of disturbed land based upon the Contractor's capability to effectively control erosion and sedimentation on these areas and contain the sediment within the right-of-way limits, including temporary construction easements (TCE). The Contractor shall be responsible for making the necessary arrangements with the proper owner(s) and for reclaiming sediment and stabilizing the area that is not contained within these limits. This work will be the responsibility of the Contractor and shall be performed at no cost to the Department.

- Cut and fill slopes shall be completed and stabilized in increments not to exceed 25 feet (8 meters), measured vertically, as the construction progresses.

- Completed areas within buffer zones adjacent to water bodies as shown on plans or otherwise designated by the Engineer, shall receive permanent seeding, temporary seeding, or mulch cover as soon as possible, but in no case more than five business days after completion, or as directed by the Engineer.

- All other completed areas, including increments of cut and fill slopes described above, shall receive permanent seeding, temporary seeding, or mulch cover within 14 calendar days after completion as directed by the Engineer.

- Disturbed areas that are temporarily abandoned shall be stabilized within 14 calendar days after activity ceases unless work is to be resumed within 21 calendar days after activity ceases. Payment for this work will be made if abandoned due to no fault or negligence of the Contractor. Payment will not be made for temporary stabilization required by Contractor negligence, by the lack of proper Contractor scheduling, or for the convenience of the Contractor.

- Excavation, including silt removed from erosion and sedimentation control devices, shall not be deposited where it can be eroded into waters of the United States. At locations of drainage structures, care shall be taken to prevent mounds of excavation on the inlet end from washing through the structure or on the outlet end from washing downstream.

- Water pumped during any dewatering activity shall be diverted into a sediment basin of the appropriate type as shown on the standard drawings or other device as approved by the Engineer. This sediment basin or device and its holding capacity shall be approved by the Engineer.  No turbid discharge to waters of the state shall be allowed.

- Off-site vehicle tracking of sediments and the generation of dust shall be minimized. The Contractor shall construct stabilized entrances to the work areas necessary by the work to eliminate off-site tracking of soils. Work involved in constructing stabilized entrances will not be measured or paid for separately, but full compensation therefore will be considered included in the contract unit prices bid for other items of the Contract. Sediment tracked from the construction site shall be removed by sweeping at a frequency to minimize off-site impacts to water bodies.

- After cut sections are constructed, the tops of backslopes will be rounded to blend the slopes into natural ground when practicable. At transitions from cut to fill, ditches shall be tailed out to prevent erosion of the toe of slope.

- Temporary erosion and sedimentation control devices shall not be removed or destroyed by the Contractor without permission from the Engineer.

Additional temporary and permanent erosion and sedimentation control items necessary on the right-of-way to contain discharges not attributed to the Contractor's negligence, carelessness, or failure to install permanent controls, shall be performed as ordered by the Engineer and will be paid for either at unit bid prices or as provided for in Subsection 109.04.

110.06 Pollutants. (a) General. The Contractor shall employ best management practices to prevent pollution by spills. Pollutants such as chemicals, fuels, lubricants, asphalt, raw sewage, concrete drum wash water, and other harmful wastes shall not be discharged into or alongside any waters of the United States, but shall be disposed of in accordance with governing State and Federal regulations. Storage of these materials shall not be allowed within 100 feet (30 meters) of a wetland or waterbody.

(b) Spill Prevention.

(1) Good Housekeeping.

- The quantity of materials stored on the project should be limited, as much as practical, to that quantity required to perform the work in an orderly sequence and should be stored in a neat, orderly manner in their original containers with the original manufacturer's label.

- Manufacturer's recommendations for proper use and disposal of materials shall be followed. All disposal shall be according to all local, State and Federal regulations in a permitted landfill or permitted disposal facility.

- The Contractor should inspect daily to ensure proper use and disposal of materials.

(2) Hazardous Products.

- Hazardous products shall be kept in original containers with their original labels unless they are not re-sealable or are damaged.

- Material Safety Data Sheets shall be retained and shall be available to all personnel at all times.

- If surplus products must be disposed of, manufacturer's recommendations and local, State, and Federal regulations shall be followed.

(3) Product Specific Practices. The Contractor shall limit the amount of petroleum products and other chemicals in work areas adjacent to wetlands, water bodies, and other sensitive areas. The following product specific practices shall be followed on-site:

- Petroleum Products. All on-site vehicles shall be monitored for leaks and receive regular preventive maintenance to reduce the chance of leakage. Petroleum products shall be stored in tightly sealed containers that are clearly labeled. All asphalt substances used on-site shall be applied according to manufacturer's recommendations and/or Department specifications. Construction of berms, or other similar measures, may be required for storage/refueling areas as a best management practice to restrict spill areas.

- Fertilizers. Fertilizers shall be applied only in the manner and amounts required by the specifications. Material shall be stored in a covered area and shall not be exposed to precipitation. Partially used bags shall not be discarded, but removed and disposed of properly. No storage of these materials shall be allowed within a wetland or floodplain.

- Paints and Solvents. All containers shall be tightly sealed and stored when not required for use. Excess material and waste shall not be discharged, but shall be properly disposed of according to manufacturers' instructions and/or State and Federal regulations. No storage of these materials shall be allowed within a wetland or floodplain.

- Concrete Trucks. Concrete trucks shall be allowed to discharge surplus concrete or drum wash water on site only in areas designated in the SWPPP. Discharge areas shall not be in or where the discharge can be washed into wetlands or waterbodies.

- Concrete Curing Agents. Concrete curing agents shall be applied only in the manner and amount required by the specifications. Excess material shall not be allowed to run off the area being treated.

(c) Spill Reporting and Cleanup Practices. All spills shall be reported as described in Subsection 107.01(f).

In addition, the practices below shall be followed:

- All spills shall be cleaned up immediately after discovery or contained until appropriate cleanup methods can be employed.

- The spill area shall be contained and personnel shall wear appropriate protective clothing to prevent injury from contact with a hazardous substance.

- Manufacturer's recommended methods for spill cleanup shall be followed along with proper disposal methods in accordance with local, State, and Federal regulations.

Further, where a release containing a hazardous substance or oil in an amount equal to or in excess of a reportable quantity established under either 40 CFR §§ 110, 117, or 302, occurs on the right-of-way during a 24-hour period, the following action shall be taken by the Engineer:

- A report shall be submitted to the Arkansas Department of Environmental Quality within 14 calendar days of the knowledge of the release. The report shall include a written description of the release (including the type and estimate of the amount of material released); the date that such a release occurred; the circumstance leading to the release; and the corrective actions taken.

- The Storm Water Pollution Prevention Plan must be modified within 14 calendar days of knowledge of the release by addition of the above information. Review and modification of the plan must be made to identify measures to prevent the recurrence of such releases, and to respond to such releases.

If the spill occurs on a site off of the right-of-way, the Contractor shall follow the reporting procedures as described above.

110.07 Contractor Negligence. If the Contractor violates the requirements of a C of E Section 404 Permit, NPDES Permit, or any other requirement of these specifications, and fails to properly maintain, install and/or construct erosion and siltation control items, the Engineer may take, but is not limited to, one or more of the following actions:

• Cessation of other project related work,

• Withholding of Contractor payments,

• Suspension of the Project,

• Default of the Contract.

All work required due to the violation of provisions of C of E Section 404, NPDES Permits, or other requirements of these specifications which results from Contractor negligence, carelessness, or failure to perform work as scheduled, shall be performed by the Contractor at no cost to the Department. In addition, the Contractor will be assessed the amounts of any and all fines and penalties assessed against and costs incurred by the Department which are the result of the Contractor's failure to comply with a C of E Section 404 Permit or NPDES Permit.

Failure to comply with the conditions of the C of E Section 404 Permit may result in the C of E issuing a cease and desist order for all permitted activities. Obtaining a new Section 404 Permit from the C of E may require 60-120 calendar days processing time.

The Department will not be responsible for any delays or costs due to the Contractor's failure to comply with the above special conditions. The Contractor will not be granted additional compensation or contract time due to loss of Permits for noncompliance.

In the event that pollutant spills occur which are the result of the Contractor's actions or negligence, the clean up shall be performed by the Contractor at no cost to the State.

110.08 Method of Measurement and Basis of Payment. Work required to comply with this subsection will not be paid for separately but will be considered included in the unit prices bid for other items of the work.