## Slide 1: Smarter Work Zones
Duane Thomas, PE
FHWA – Resource Center
Operations Technical Services Team
August 15, 2019

## Slide 2: Smarter Work Zones (SWZ)
Innovative strategies designed to optimize work zone safety and mobility
Policies and practices used to incrementally and continuously improve WZ operations
Tools to reduce WZ crashes and delays
Tools to enhance WZ management strategies

## Slide 3: Negative Consequences of Work Zones
Source: Fatality Analysis Reporting System (FARS) 2016 Final and 2017 Annual Report File, National Highway Traffic Safety Administration (NHTSA).

## Slide 4: Negative Consequences of Work Zones
8 times higher than the rate of all workers
2 times the rate of other construction workers
Source: 2016 and 2017 U.S. Department of Labor, Bureau of Labor Statistics

## Slide 5: Negative Consequences of Work Zones
Source: Fatality Analysis Reporting System (FARS) 2015 and 2016 Final and 2017 Annual Report File, National Highway Traffic Safety Administration (NHTSA).

## Slide 6: Negative Consequences of Work Zones
Arkansas WZ Fatalities
Source: Fatality Analysis Reporting System (FARS), National Highway Traffic Safety Administration (NHTSA).
Ranked 10th in the US for 2017

## Slide 7: Negative Consequences of Work Zones
Source: Fatality Analysis Reporting System (FARS) 2016 Final and 2017 Annual Report File, National Highway Traffic Safety Administration (NHTSA).

## Slide 9: Negative Consequences of Work Zones
Source: Fatality Analysis Reporting System (FARS) 2016 Final and 2017 Annual Report File, National Highway Traffic Safety Administration (NHTSA).

## Slide 10: Work Zones: Scope and Scale
Exposure: Part of the Driving Experience
Over 11 billion VMT through construction
  One active WZ encountered per 100 miles driven on the NHS, representing over 12 billion hours of vehicle exposure nationally; half involve lane closures
  Work Zone related mobility impact:
  10% (total congestion)
  25% (non-recurring congestion)

## Slide 11: Can we do better?

## Slide 12: SWZ Strategies
SWZ Initiative #1: Project Coordination
      Coordination within a single project and/or among multiple projects within a corridor, network, or region, and possibly across agency jurisdictions
      SWZ Initiative #2: Technology Application
      Deployment of Intelligent Transportation Systems (ITS) for dynamic management of work zone traffic impacts, such as queue and speed management

## Slide 13: Smarter Work Zones Project Coordination Examples

## Slide 14: Project Coordination Guide
Organized by the five steps for achieving project coordination:
  Step 1: Establishing the Project Coordination Vision
  Step 2: Developing Details of How Coordination will Occur
  Step 3: Educating and Informing Personnel and Stakeholders
  Step 4: Implementing the Project Coordination Process
  Step 5: Refining the Process
https://ops.fhwa.dot.gov/wz/construction/crp/index.htm
  Publication FHWA-HOP-16-013
  Available in PDF only

## Slide 15: PC Strategy #1 Software to coordinate right-of-way construction activities
Baltimore, MD: Online mapping tool used to track capital and maintenance/utility activities
  Real-time information across city
  Accessible to all stakeholders
  Earlier awareness of project conflicts/impacts and enhanced TMPs
Washington, DC: WZ Project Management System
  System includes:
    DDOT, Developer, Utility WZ Projects
    Work Zone Tracking Tool
    Traffic Analysis Tool
  Used to develop annual citywide TMP
  Tracks performance measurement
Source: DDOT

## Slide 16: PC Strategy #2 Corridor-level TMPs to address traffic-related construction impacts
Oregon Transportation Investment Act
  Significant construction
  Six corridors identified
  Three levels of TMP
  Corridor-Level TMPs
    Assess corridor traffic impacts
    Define corridor/segment
    delay thresholds
    Suggest traffic mgmt. strategies
    Discuss implementation plan

## Slide 17: PC Strategy #3 Multi-agency construction traffic management activities
Washington State DOT
  Collaborative, multi-agency construction traffic planning effort
  Long-term, mid-term, and short-term information sharing
  Construction Impact Analysis Tool, Maps, Gantt Charts
  Hot Spots, Watch Lists

## Slide 18: PC Strategy #4 Building partnerships to enhance mobility during construction
Michigan’s I-94 Corridor
  I-94 Corridor Operation Partnership (COP) Mission: “Improve traffic operations and system reliability along the I‐94 corridor statewide.”
  I-94 COP Objectives:
    Unification of I-94 corridor with one focus
    Travel Reliability: 40 min delay max for entire corridor

## Slide 19: Smarter Work Zones Technology Application Examples

## Slide 20: Work Zone ITS Implementation Guide
  Work Zone ITS Implementation Guide
  Publication FHWA-HOP-14-008
  Available in print & PDF ops.fhwa.dot.gov/publications/fhwahop14008/
  Work Zone ITS Case Studies
  Publication FHWA-HOP-14-007
  Available in PDF only
  ops.fhwa.dot.gov/publications/fhwahop14007/

## Slide 21: WZ ITS Implementation Tool
Software companion tool to the Guide to help bridge the gap between principles and practice
Follows logic and methodology descried in the Guide, extends its usefulness by leading the user through the process outlined in the guide

## Slide 22: Primary Tool Functions
Technical Recommendations  Provide specific recommendation of what ITS technology to consider as a result of the inputs provided.
Project Management Tool  Guide the user through the various steps and sub-steps of the Guide and assist with data entry and general navigation of the WZITS process. The tool clearly establishes the sequence of decision-making, and facilitates use of the Guide.
Content Management Tool  Establish a record of decision-making and store interim information from the various steps in the guide, including listing of outputs, contact information for stakeholders, and records of decisions made along the way.

## Slide 23: Obtaining the Tool
Download Tool and User Guide at https://itsforge.net/
  The Open Source Application Development Portal (OSADP) is a web-based portal that provides access to and supports the collaboration, development, and use of open-source intelligent transportation systems (ITS)-related applications

## Slide 24: TA Strategy #1 Queue Warning System (QWS)
Work Zone
Warning Signs installed per TCP
Zone of advanced work zone awareness provided by Queue Warning System
STOPPED
TRAFFIC
2 MILES
Queue Detection Zone
Queue Warning Controller
data
PCMS

## Slide 25: TA Strategy #2 Variable Speed Limits (VSL)
  Multiple speed trailers in & approaching work zone
  Each unit monitors prevailing speed-relays information to upstream units
  Posted speed limit dynamically adjusted to reduce downstream speed differentials

## Slide 26: TA Strategy #3 Dynamic Lane Merge
Early Merge
  In low-volume conditions reduces the occurrence of high-speed merging at the point of lane closure
Late Merge
  In high-volume conditions reduces the length of the queue
Source: Maryland State Highway Administration

## Slide 27: TA Case Study #1 I-35 Traveler Information During Construction
  Provide advance notification of planned lane closures and their anticipated impacts
  Provide travelers with predicted delays for construction closures (web app http://i35-maps.tti.tamu.edu/
  Provide real-time traveler information

## Slide 28: TA Case Study #2 Rural Queue Detection and Warning System
Central Illinois reconstruction projects used ITS for WZ rear-end crash concerns
  I-70/I-57 interchange, 6 mi of concurrent routes
  I-57/I-64 Interchange, 4 mi of concurrent routes
Key Concerns
  Unpredictable queues leading to severe rear-end crashes
  Lengthy delays when queues form
Solution Requirements
  Automatic detection of slow/queued traffic
  Ability to warn approaching motorists of slow/queued traffic
  Encourage diversion by informing motorists of current delays
Temporary, solar-powered system
FHWA
FHWA

## Slide 29: TA Case Study #2 (cont.) Rural Queue Detection and Warning System
I-70/I-57 Interchange
  Portable solar-powered trailers:
    Radar sensors
    Traffic sensors
    Video surveillance cameras
  Traffic volume and speed data across multiple lanes of traffic
  Sensors not degraded by inclement weather conditions:
    Precipitation, fog, darkness, dust, or road debris
  Cellular communications
Limits of the I-70/I-57 WZTMS
(10-12 miles upstream in each direction)

## Slide 30: TA Case Study #2 (cont.) Rural Queue Detection and Warning System
I-57/I-64 Interchange
  Portable traffic monitoring devices
  Self-contained, battery-powered unit with radar detector, GPS, cellular, and backup satellite communication capabilities and processors
  Sensors 3-14 miles upstream of interchange (depending on direction)
I-57/I64 Map layout of sensors

## Slide 31: Resources

## Slide 32: http://www.ops.fhwa.dot.gov/wz/resources/final_rule.htm

## Slide 33: SWZ Interactive Toolkit
https://www.workzonesafety.org/swz/

## Slide 34: FHWA WZM Website

## Slide 35: FHWA Work Zone Management Web Site
Facts & Statistics
Best Practices
Contracting Strategies
Design & Construction Strategies
ITS & Technology
Performance Measurement
WZ Process Review Toolbox
Public Info Strategies
Regulation & Policy
Work Zone Final Rules
Work Zone & Traffic Analysis
Work Zone Traffic Management
Worker Safety
Training
Peer-to-Peer Program
National WZ Awareness Week
Publications & Studies
35
https://ops.fhwa.dot.gov/wz/
Notes: The FAQs are very helpful.

## Slide 36: FWHA SWZ Support
  SWZ outreach materials
  Toolkit (online)
  Webinar recordings, case studies and fact sheets
  Virtual and in-person training opportunities
  1-2 day in-person workshops
  Virtual and in-person peer-to-peer exchanges
  Hosting and participant opportunities
  Regional Peer Exchange Workshops
  Hosting and participant opportunities
  Demonstration Site Visits
  Hosting and participant opportunities
  Learn more about SWZ strategies and deployments!
  Learn about SWZ concepts based on YOUR state needs!
  See first-hand SWZ deployments across the country!
  Meet with agencies who have successfully adopted SWZ strategies!

## Slide 37: Contact Information
Duane Thomas, PE
FHWA – Resource Center
Operations Technical Services Team
Duane.Thomas@dot.gov